## Slide 1: Prof.mrs najma siddiqui
ANJUMAN COLLEGE OF ENGINEERING & TECHNOLOGY
Department of Electrical Engineering
SUB:- Basic Electrical Engineering

## Slide 2: Unit I : Single Phase Transformers
Objectives: To understand-
Principle of operation of Single phase transformer,
Construction and types of Single phase transformer,
Concept of ideal transformer,
Operation at no load,
Operation on load,
Losses in transformer,
Open circuit test to determine core losses,
Short circuit test to determine copper losses,
Performance indices i.e. Efficiency and Voltage regulation,
Concept of maximum efficiency, condition for maximum efficiency,
Concept of Autotransformer, construction, kVA rating & saving of copper,
Applications

## Slide 3: Definition of transformer:
Transformer is defined as
a static device
works on mutual induction
transforms electric power from one circuit to the other without any electric connection between them
at desired voltage level
without any change in frequency
Fig. 1.1 : Explanation of Transformer Definition

## Slide 4: Principle of operation:
Transformer works on the basic principle of Electro-magnetic induction by Faraday which states that ‘ ‘ ‘Whenever a coil links with a changing magnetic flux, an EMF is induced in the coil’ and
‘This induced EMF is numerically equal to the rate of change flux linkages of the coil’
‘The induced EMF opposes the very cause of its own production, as per Lenz’s law.
Hence, the induced EMF is given by: e = - d/dt (Nφ)
Fig. 1.2 Principle of Operation
Two coils being provided
on the common magnetic circuit are inductively coupled and when current in any one of these coils is changed uniformly, an emf is induced in the other coil.

## Slide 5: Transformation Ratio:
On neglecting losses in the transformer, its input shall be equal to output
i.e. V1I1 = V2I2
Dividing both sides by V1I2,
V2/V1 = E2/E1 = N2/N1 = I1/I2 = K
where K is known as Transformation ratio.
Ratio of turns on primary side to that of secondary side, N1/N2 = a . . . (Turns Ratio)
Transformation and Turns ratio are thus
k = 1/a

## Slide 6: Theory of transformer operation:
AC supply when connected to primary winding of Transformer on no load, a current Io ∟-φ0 is drawn by the transformer for magnetizing the core and supplying core losses.
Magnetizing current,
Iµ = I0 Sinφ0
Core loss component,
Iw = I0 Cosφ0
So that, I0 = Iw - jIµ
Current I0 flowing through N1 turns of primary sets up an mmf N1I1 , which in turn sets up flux in core.
This flux links with both windings inducing EMFs E1(opposing V1) in primary and E2 in secondary wdgs.

## Slide 7: Theory of transformer operation (Contd…):
When load is connected across the secondary winding, the induced emf E2 drives current I2 through the load.
Current I2 flowing through N2 turns of secondary winding sets up flux φ2 in the core, in opposition to flux φ0.
Net flux being reduced, E1 reduces in magnitude. As a result V1 gets an upper hand over E1 and a larger current I1 = I0 + I2’ is drawn, where I2’= -kI2 is drawn for negating mmf setup by secondary current I2.
Flux φ2’ being equal but opposite to φ2, net flux (hence flux density) in the core remains almost constant, from no load to full load.
WEddy(αB2) & Whysteresis (αB1.6) are constant.

## Slide 8: Emf equation of a transformer:
Flux setup in the core varies
sinusoidally & given by
ø = Φm cosωt ..As ø0 = Φm & øπ/2 = 0
EMF induced in a winding , as per
law’s of EMI is e = - d(Nø)/dt
or e = - d(NΦm cosωt)
or e = NωΦmsinωt
The equation is in form, e = Emsin ωt
i.e. Em = NωΦm = 2πNfΦm (Em: Peak Value)
RMS value of EMF induced in winding,
Eph = Em/√2 = (2π/√2)NfΦm
Or Eph= 4.44 NfΦm …EMF Equation
Prim. wdg. emf, E1 = 4.44N1fΦm volts, & Second. wdg. emf, E2 = 4.44N2fΦmvolts
Core Flux Waveform
EMF Waveform

## Slide 9: Concept of ideal transformer:
Ideal transformer is a hypothetical concept.
It is assumed to have following properties:
It has efficiency of 100%, as
It has no copper loss ( Both winding resistances negligible),
It has no core losses (Loss component, Iw = 0)
Core has infinite permeability,µ (Negligible magnetizing current, Iµ)
It has Zero voltage regulation, as
Entire flux is setup in the core, ( No leakage flux & hence no leakage reactances )
Both windings are resistance free
It operates at load power factor

## Slide 10: Practical transformer:
Ideal transformer is a hypothetical concept of a perfect transformer, but a practical transformer has following imperfections:
  R1 & R2 represent primary &
  secondary winding resistances resp.
  Voltage drops in the resp. windings
  are I1R1 & I2R2.
Winding Resistance: Windings of
a transformer, being made of
Cu wire, have some resistance.
Resistance of a winding is
considered by connecting
resistance in series with the
ideal winding.

## Slide 11: Practical transformer (Contd…) :
Leakage Flux: There being no good insulator of magnetic field, entire flux produced by a winding is not set up along intended path. Part of the flux links with the winding itself and is k/as Leakage flux.
Effect of leakage flux is to induce emf in the winding, in opposition to the cause producing it. As the leakage flux is not contributing towards transfer of electric power, this induced emf is considered as voltage drop in an imaginary reactance.
  X1 & X2 represent primary &
  secondary winding leakage
  reactances resp.
  Voltage drops in the resp.
  windings are jI1X1 & jI2X2.

## Slide 12
Practical transformer (Contd…) :
Each winding of the transformer has a resistance and a
leakage reactance.
Voltage equations for the
two sides are:
E1 = V1 – I1R1 – jI1X1, and
V2 = E2 – I2R2 – jI2X2
Vector diagram for 2’ary
side is drawn for load
power factor with terminal
voltage as ref. vector. This
V.D. is rotated by –(90°+δ)
to project E2 vertically down.
Quantities on primary side
are drawn on the same
diagram, as shown to get
vector diagram of the
transformer at desired p.f.
V.D. for load side
V.D. of transformer on load at lag p.f.

## Slide 13
LOSSES IN TRANSFORMER:
Two types of losses occur in a transformer:
1. Core loss or iron loss occur in iron core due to alternating
flux set up in it, and
2. Copper loss occurs in the windings due to current flowing
in them on loading the transformer.
Core Loss: These are of two types,
a. Eddy current loss, and b. Hysteresis loss
Eddy Current Loss: Emf induced in the core sets up eddy
current in the core, in turn eddy current loss occurs and is
given by WE= Ke Bm2f2t2 Watts, where Ke is eddy current
constant, t is thickness of the core.
Hysteresis Loss: Mag. Core exhibits property of lagging of the
flux density behind the magnetizing force when subjected to an
alternating flux. This property k/as hysteresis causes energy
loss, This loss is given by WH = KhBm1.6fV Watts
Copper Loss: This is loss of power due to heat produced by
currents in the windings. It is given by
Pcu = I12R1 + I22R2 = I12R01= I22R02

## Slide 14
THANK YOU