## Slide 1: Tariff

## Slide 2: The rate at which energy is sold to the consumers (called tariff) is fixed by the supplying company
IMPORTANT TERMS
Connected load: The sum of the continuous ratings of all the equipments connected to the power system is called connected load.
Maximum Demand: The load on the power station is not constant, it varies from time to time. The greatest of all the demands (loads) which occur during a given period is called maximum demands.
The ratio of maximum demand on the system to the rated connected load to the system is called demand factor.
Mathematically, Demand factor = Maximum demand
Connected load

## Slide 3: Objective Tariff
Recovery of cost of electrical energy generated at the generating system.
Recovery of cost on the capital investment in transmission and distribution system.
Recovery of cost of operation, supplies and maintenance of equipment.
Recovery of cost of metering equipment, billing and miscellaneous services .
A marginal return (Profit) on the capital investment

## Slide 4: TYPES OF TARIFF
SIMPLE TARIFF
FLAT RATE TARRIF
BLOCK RATE TARIFF
TWO-PART TARIFF
MAXIMUM DEMAND TARIFF
POWER FACTOR TARIFF

## Slide 5: Simple Tariff
The tariff in which the rate per unit of energy is fixed, is called simple tariff.
Advantages
  1. It is in simplest form and easily understood by the consumers.
2. Consumer is to pay as per his consumption.
Disadvantages
1. Consumer is to pay the same rate per unit of energy consumed irrespective of the number of units consumed by him. Hence, consumers are not encourage to consume more energy.
2. The supplier does not get any return for the connection given to the consumer if consumer does not consume any energy in a particular month.

## Slide 6: Flat rate tariff
The tariff in which different types of consumers are charged at different per unit rates is called flat rate tariff.
Advantages
1. It is fairer to different types of consumers.
2. It is quite simple in calculations.
Disadvantages
1. Separate meters are required to measured energy consumed for light loads and power loads.
2. The suppliers does not get any return for the connection given to the consumer if he does not consume any energy in a particular period or month.

## Slide 7: block rate tariff
The tariff in which first block of energy is charged at a given rate and the succeeding blocks of energy are charged at progressively reduced rates is called block rate tariff
Advantages:
1. Only one energy meter is required to measure the energy .
Disadvantages:
1. The supplier does not get any return for the connection given to the consumer if consumer does not consume any energy in a particular period.

## Slide 8: Two – Part Tariff
The tariff in which electrical energy is charged on the basis of maximum demand of the consumer and the units consumed by him is called two- part tariff.
Advantages
1. It is easily understood by the consumers.
2. The supplier gets the return in the form of fixed charges for the connection given to the consumer even if he does not consume any energy in a particular period.
Disadvantages
1. If a consumer does not consume any energy in a month even then he has to pay the fixed charges .
2. Since the maximum demand of consumer is not measured, therefore, there is always conflict between consumer and the supplier to assess the maximum demand.

## Slide 9
THANK YOU