## Slide 1
Anjuman college of engineering
Department of electronics & telecommunication
Course Name : Analog circuit design
Unit 1 - Operational Amplifier
Prepared by: Mohsina Anjum

## Slide 2: Reference books used: 1. Linear Integrated Circuits – D. Roy Choudhury 2. Op-Amps & Linear ICs – Ramakanth A. Gayakwad. 3. Digital Fundamentals – Floyd and Jain

## Slide 3: Unit 1- Operational amplifies
What is an Integrated Circuit?
Where do you use an Integrated Circuit?
Why do you prefer an Integrated Circuit to the circuits made by interconnecting discrete components?

## Slide 4: Def: The “Integrated Circuit “ or IC is a miniature, low cost electronic circuit consisting of active and passive components that are irreparably joined together on a single crystal chip of silicon.
In 1958 Jack Kilby of Texas Instruments invented first IC

## Slide 5
Communication
Control
Instrumentation
Computer
Electronics
Applications of an Integrated Circuit

## Slide 6
Small size
Low cost
Less weight
Low supply voltages
Low power consumption
Highly reliable
Matched devices
Fast speed
Advantages:

## Slide 7: Classification
Digital ICs
Linear ICs
Pn junction
isolation
Hybrid circuits
Integrated circuits
Dielectric
isolation
Monolithic circuits
Bipolar
Uni polar
MOSFET
JFET
Classification of ICs
Thick &Thin film

## Slide 8: Chip size and Complexity
Invention of Transistor (Ge) - 1947
Development of Silicon - 1955-1959
Silicon Planar Technology - 1959
First ICs, SSI (3- 30gates/chip) - 1960
MSI ( 30-300 gates/chip) - 1965-1970
LSI ( 300-3000 gates/chip) -1970-1975
VLSI (More than 3k gates/chip) - 1975
ULSI (more than one million active devices are integrated on single chip)

## Slide 9
SSI | MSI | LSI | VLSI | ULSI
< 100 active devices | 100-1000 active devices | 1000-100000 active devices | >100000 active devices | Over 1 million active devices
Integrated resistors, diodes & BJT’s | BJT’s and Enhanced MOSFETS | MOSFETS | 8bit, 16bit Microprocessors | Pentium Microprocessors

## Slide 10: IC Package types
Metal can Package
Dual-in-line
Flat Pack

## Slide 11: Metal can Packages
The metal sealing plane is at the bottom over which the chip is bounded
It is also called transistor pack

## Slide 12: Doul-in-line Package
The chip is mounted inside a plastic or ceramic case
The 8 pin Dip is called MiniDIP and also available with 12, 14, 16, 20pins

## Slide 13: Flat pack
The chip is enclosed in a rectangular ceramic case

## Slide 14
Selection of IC Package
Type | Criteria
Metal can package | Heat dissipation is important For high power applications like power amplifiers, voltage regulators etc.
DIP | For experimental or bread boarding purposes as easy to mount If bending or soldering of the leads is not required Suitable for printed circuit boards as lead spacing is more
Flat pack | More reliability is required Light in weight Suited for airborne applications

## Slide 15
The metal can (TO)
Package
The Dual-in-Line (DIP) Package
The Flat Package
Packages

## Slide 16: Factors affecting selection of IC package
Relative cost
Reliability
Weight of the package
Ease of fabrication
Power to be dissipated
Need of external heat sink

## Slide 17
Military temperature range : -55o C to +125o C (-55o C to +85o C)
Industrial temperature range : -20o C to +85o C (-40o C to +85o C )
Commercial temperature range: 0o C to +70o C (0o C to +75o C )
Temperature Ranges

## Slide 18: Manufacturer’s Designation for Linear ICs
Fairchild - µA, µAF
National Semiconductor - LM,LH,LF,TBA
Motorola - MC,MFC
RCA - CA,CD
Texas Instruments - SN
Signetics - N/S,NE/SE
Burr- Brown - BB

## Slide 19: Operational Amplifier
An “Operational amplifier” is a direct coupled high-gain amplifier usually consisting of one or more differential amplifiers and usually followed by a level translator and output stage.
The operational amplifier is a versatile device that can be used to amplify dc as well as ac input signals and was originally designed for computing such mathematical functions as addition, subtraction, multiplication and integration.

## Slide 20: Op Amp
Non-inverting
Input terminal
Inverting input
terminal
Output terminal
Positive power supply (Positive rail)
Negative power supply
(Negative rail)

## Slide 21: The Op-Amp Chip
741 Op Amp or LM351 Op Amp

## Slide 22
Op-amp have 5 basic terminals(ie 2 i/p’s 1 o/p and 2 power supply terminals
The output goes positive when the non-inverting input (+) goes more positive than the inverting (-) input, and vice versa.

## Slide 23: Single-Ended Input
Ref:080114HKN
Operational Amplifier
23
+ terminal : Source
– terminal : Ground
0o phase change
+ terminal : Ground
– terminal : Source
180o phase change

## Slide 24: Basic Information of Op-Amp
Op-amps have five basic terminals, that is, two input terminals, one output terminal and two power supply terminals.

## Slide 25
Basic Information of an Op-amp contd…
Power supply connection:
The power supply voltage may range from about + 5V to + 22V.
The common terminal of the V+ and V- sources is connected to a reference point or ground.

## Slide 26: Differential Amplifier
V0 =Ad (V1 – V2 )
Ad =20 log10 (Ad ) in dB
Vc =
CMRR= ρ = | |

## Slide 27: Characteristics and performance parameters of Op-amp
Input offset Voltage
Input offset current
Input bias current
Differential input resistance
Input capacitance
Open loop voltage gain
CMRR
Output voltage swing

## Slide 28: Characteristics and performance parameters of Op-amp
Output resistance
Offset adjustment range
Input Voltage range
Power supply rejection ratio
Power consumption
Slew rate
Gain – Bandwidth product
Equivalent input noise voltage and current

## Slide 29: Characteristics and performance parameters of Op-amp
Average temperature coefficient of offset parameters
Output offset voltage
Supply current

## Slide 30: 1. Input Offset Voltage
The differential voltage that must be applied between the two input terminals of an op-amp, to make the output voltage zero.
It is denoted as Vios
For op-amp 741C the input offset voltage is 6mV

## Slide 31: 2. Input offset current
The algebraic difference between the currents flowing into the two input terminals of the op-amp
It is denoted as Iios = | Ib1 – Ib2|
For op-amp 741C the input offset current is 200nA

## Slide 32: 3. Input bias current
The average value of the two currents flowing into the op-amp input terminals
It is expressed mathematically as
For 741C the maximum value of Ib is 500nA

## Slide 33: 4. Differential Input Resistance
It is the equivalent resistance measured at either the inverting or non-inverting input terminal with the other input terminal grounded
It is denoted as Ri
For 741C it is of the order of 2MΩ

## Slide 34: 5. Input capacitance
It is the equivalent capacitance measured at either the inverting or non- inverting input terminal with the other input terminal grounded.
It is denoted as Ci
For 741C it is of the 1-4 pF

## Slide 35: 6. Open loop Voltage gain
It is the ratio of output voltage to the differential input voltage, when op-amp is in open loop configuration, without any feedback. It is also called as large signal voltage gain
It is denoted as AOL
AOL=Vo / Vd
For 741C it is typically 200,000

## Slide 36
7. CMRR
It is the ratio of differential voltage gain Ad to common mode voltage gain Ac
CMRR = Ad / Ac
Ad is open loop voltage gain AOL and Ac = VOC / Vc
For op-amp 741C CMRR is 90 dB

## Slide 37
8. Output Voltage swing
The op-amp output voltage gets saturated at +Vcc and –VEE and it cannot produce output voltage more than +Vcc and –VEE. Practically voltages +Vsat and –Vsat are slightly less than +Vcc and –VEE .
For op-amp 741C the saturation voltages are + 13V for supply voltages + 15V

## Slide 38: 9. Output Resistance
It is the equivalent resistance measured between the output terminal of the op-amp and ground
It is denoted as Ro
For op-amp 741 it is 75Ω

## Slide 39: 10. Offset voltage adjustment range
The range for which input offset voltage can be adjusted using the potentiometer so as to reduce output to zero
For op-amp 741C it is + 15mV

## Slide 40: 11. Input Voltage range
It is the range of common mode voltages which can be applied for which op-amp functions properly and given offset specifications apply for the op-amp
For + 15V supply voltages, the input voltage range is + 13V

## Slide 41: 12. Power supply rejection ratio
PSRR is defined as the ratio of the change in input offset voltage due to the change in supply voltage producing it, keeping the other power supply voltage constant. It is also called as power supply sensitivity (PSV)
PSRR= (Δvios / ΔVcc)|constant VEE
PSRR= (Δvios / ΔVEE)|constant Vcc
The typical value of PSRR for op-amp 741C is 30µV/V

## Slide 42: 13. Power Consumption
It is the amount of quiescent power to be consumed by op-amp with zero input voltage, for its proper functioning
It is denoted as Pc
For 741C it is 85mW

## Slide 43: 14. Slew rate
It is defined as the maximum rate of change of output voltage with time. The slew rate is specified in V/µsec
Slew rate = S = dVo / dt |max
It is specified by the op-amp in unity gain condition.
The slew rate is caused due to limited charging rate of the compensation capacitor and current limiting and saturation of the internal stages of op-amp, when a high frequency large amplitude signal is applied.

## Slide 44: Slew rate
It is given by dVc /dt = I/C
For large charging rate, the capacitor should be small or the current should be large.
S = Imax / C
For 741 IC the charging current is 15 µA and the internal capacitor is 30 pF. S= 0.5V/ µsec

## Slide 45: Slew rate equation
Vs = Vm sinωt
Vo = Vm sinωt
S =slew rate =
= Vm ω cosωt
max
S = Vm ω = 2 π f Vm
S = 2 π f Vm V / sec
For distortion free output, the maximum allowable input frequency fm can be obtained as
This is also called full power bandwidth of the op-amp

## Slide 46: 15. Gain – Bandwidth product
It is the bandwidth of op-amp when voltage gain is unity (1). It is denoted as GB.
The GB is also called unity gain bandwidth (UGB) or closed loop bandwidth
It is about 1MHz for op-amp 741C

## Slide 47: 16. Equivalent Input Noise Voltage and Current
The noise is expressed as a power density
Thus equivalent noise voltage is expressed as V2 /Hz while the equivalent noise current is expressed as A2 /Hz

## Slide 48: 17. Average temperature coefficient of offset parameters
The average rate of change of input offset voltage per unit change in temperature is called average temperature coefficient of input offset voltage or input offset voltage drift
It is measured in µV/oC. For 741 C it is 0.5 µV/oC
The average rate of change of input offset current per unit change in temperature is called average temperature coefficient of input offset current or input offset current drift
It is measured in nA/oC or pA/oC . For 741 C it is 12 pA/oC

## Slide 49: 18. Output offset voltage ( Voos )
The output offset voltage is the dc voltage present at the output terminals when both the input terminals are grounded.
It is denoted as Voos

## Slide 50: 19. Supply current
It is drawn by the op-amp from the power supply
For op-amp 741C it is 2.8mA

## Slide 51: Op amp equivalent circuit

## Slide 52: Block diagram of op amp

## Slide 53
The Inverting Amplifier

## Slide 54: Analyzing the Inverting Amplifier
inverting input (-):
non-inverting input (+):
1)

## Slide 55: Inverting Amplifier Analysis

## Slide 56
The Non-Inverting Amplifier

## Slide 57: Analysis of Non-Inverting Amplifier
Note that step 2 uses a voltage divider to find the voltage at VB relative to the output voltage.

## Slide 58: Comparison of the ideal inverting and non-inverting op-amp
Ideal Inverting amplifier | Ideal non-inverting amplifier
1. Voltage gain=-Rf/R1 | 1. Voltage gain=1+Rf/R1
2. The output is inverted with respect to input | 2. No phase shift between input and output
3. The voltage gain can be adjusted as greater than, equal to or less than one | 3. The voltage gain is always greater than one
4. The input impedance is R1 | 4. The input impedance is very large

## Slide 59: The Ideal Operational Amplifier
Open loop voltage gain AOL = ∞
Input Impedance Ri = ∞
Output Impedance Ro = 0
Bandwidth BW = ∞
Zero offset (Vo = 0 when V1 = V2 = 0) Vios = 0
CMRR ρ = ∞
Slew rate S = ∞
No effect of temperature
Power supply rejection ratio PSRR = 0

## Slide 60: Ideal Op-amp
An ideal op-amp draws no current at both the input terminals I.e. I1 = I2 = 0. Thus its input impedance is infinite. Any source can drive it and there is no loading on the driver stage
The gain of an ideal op-amp is infinite, hence the differential input Vd = V1 – V2 is essentially zero for the finite output voltage Vo
The output voltage Vo is independent of the current drawn from the output terminals. Thus its output impedance is zero and hence output can drive an infinite number of other circuits

## Slide 61: Op-amp Characteristics
DC Characteristics
        Input bias current
        Input offset current
        Input offset voltage
        Thermal drift
AC Characteristics
        Slew rate
        Frequency response

## Slide 62: Ideal Voltage transfer curve
+Vsat
-Vsat
0
+Vd
-Vd
AOL = ∞
+Vsat ≈ +Vcc

## Slide 63: Practical voltage transfer curve
If Vd is greater than corresponding to b, the output attains +Vsat
If Vd is less than corresponding to a, the output attains –Vsat
Thus range a-b is input range for which output varies linearily with the input. But AOL is very high, practically this range is very small

## Slide 64: Transient Response Rise time
When the output of the op-amp is suddenly changing like pulse type, then the rise time of the response depends on the cut-off frequency fH of the op-amp. Such a rise time is called cut-off frequency limited rise time or transient response rise time ( tr )

## Slide 65: Op-amp Characteristics
DC Characteristics
        Input bias current
        Input offset current
        Input offset voltage
        Thermal drift
AC Characteristics
        Slew rate
        Frequency response

## Slide 66: DC Characteristics Thermal Drift
The op-amp parameters input offset voltage Vios and input offset current Iios are not constants but vary with the factors
Temperature
Supply Voltage changes
Time

## Slide 67: Thermal Voltage Drift
It is defined as the average rate of change of input offset voltage per unit change in temperature. It is also called as input offset voltage drift
Input offset voltage drift =
∆Vios = change in input offset voltage
∆T = Change in temperature

## Slide 68
It is expressed in μV/0 c. The drift is not constant and it is not uniform over specified operating temperature range. The value of input offset voltage may increase or decrease with the increasing temperature
2
1
0
-1
-2
TA , ambient temp in oc
-25
0
25
50
75
-55
Slope can be of either polarities
Vios in mv
Input Offset Voltage Drift

## Slide 69: Input bias current drift
It is defined as the average rate of change of input bias current per unit change in temperature
Thermal drift in input bias current =
It is measured in nA/oC or pA/oc. These parameters vary randomly with temperature. i.e. they may be positive in one temperature range and negative in another

## Slide 70
Input bias current drift
100
80
60
40
20
-55
-25
0
25
50
75
TA ambient temp. in oC
Ib in nA

## Slide 71: Input Offset current drift
It is defined as the average rate of change of input offset current per unit change in temperature
Thermal drift in input offset current =
It is measured in nA/oC or pA/oc. These parameters vary randomly with temperature. i.e. they may be positive in one temperature range and negative in another

## Slide 72
2
1
0
-1
-2
TA , ambient temp in oc
-25
0
25
50
75
-55
Slope can be of either polarities
Iios in nA
Input Offset current Drift

## Slide 73: AC Characteristics Frequency Response
Ideally, an op-amp should have an infinite bandwidth but practically op-amp gain decreases at higher frequencies. Such a gain reduction with respect to frequency is called as roll off.
The plot showing the variations in magnitude and phase angle of the gain due to the change in frequency is called frequency response of the op-amp

## Slide 74
When the gain in decibels, phase angle in degrees are plotted against logarithmic scale of frequency, the plot is called Bode Plot
The manner in which the gain of the op-amp changes with variation in frequency is known as the magnitude plot.
The manner in which the phase shift changes with variation in frequency is known as the phase-angle plot.

## Slide 75: Obtaining the frequency response
To obtain the frequency response , consider the high frequency model of the op-amp with capacitor C at the output, taking into account the capacitive effect present
Where
AOL(f) = open loop voltage gain as a function of frequency
AOL = Gain of the op-amp at 0Hz
F = operating frequency
Fo = Break frequency or cutoff frequency of op-amp

## Slide 76
For a given op-amp and selected value of C, the frequency fo is constant. The above equation can be written in the polar form as

## Slide 77
Frequency Response of an op-amp

## Slide 78
The following observations can be made from the frequency response of an op-amp
The open loop gain AOL is almost constant from 0 Hz to the break frequency fo .
At f=fo , the gain is 3dB down from its value at 0Hz . Hence the frequency fo is also called as -3dB frequency. It is also know as corner frequency
After f=fo , the gain AOL (f) decreases at a rate of 20 dB/decade or 6dB/octave. As the gain decreases, slope of the magnitude plot is -20dB/decade or -6dB/octave, after f=fo .
At a certain frequency, the gain reduces to 0dB. This means 20log|AOL | is 0dB i.e. |AOL | =1. Such a frequency is called gain cross-over frequency or unity gain bandwidth (UGB). It is also called closed loop bandwidth.
UGB is the gain bandwidth product only if an op-amp has a single breakover frequency, before AOL (f) dB is zero.

## Slide 79
For an op-amp with single break frequency fo , after fo the gain bandwidth product is constant equal to UGB
UGB=AOL fo
UGB is also called gain bandwidth product and denoted as ft
Thus ft is the product of gain of op-amp and bandwidth.
The break frequency is nothing but a corner frequency fo . At this frequency, slope of the magnitude plot changes. The op-amp for which there is only once change in the slope of the magnitude plot, is called single break frequency op-amp.

## Slide 80
For a single break frequency we can also write
UGB= Af ff
Af = closed loop voltage gain
Ff = bandwidth with feedback
v) The phase angle of an op-amp with single break frequency varies between 00 to 900 . The maximum possible phase shift is -900 , i.e. output voltage lags input voltage by 900 when phase shift is maximum
vi) At a corner frequency f=fo , the phase shift is -450.
Fo = UGB / AOL

## Slide 82: The modes of using an op-amp
Open Loop : (The output assumes one of the two possible output states, that is +Vsat or – Vsat and the amplifier acts as a switch only).
Closed Loop: ( The utility of an op-amp can be greatly increased by providing negative feed back. The output in this case is not driven into saturation and the circuit behaves in a linear manner).

## Slide 83: Open loop configuration of op-amp
The voltage transfer curve indicates the inability of op-amp to work as a linear small signal amplifier in the open loop mode
Such an open loop behaviour of the op-amp finds some rare applications like voltage comparator, zero crossing detector etc.

## Slide 84: Open loop op-amp configurations
The configuration in which output depends on input, but output has no effect on the input is called open loop configuration.
No feed back from output to input is used in such configuration.
The opamp works as high gain amplifier
The op-amp can be used in three modes in open loop configuration they are
Differential amplifier
Inverting amplifier
Non inverting amplifier

## Slide 85: Differential Amplifier
The amplifier which amplifies the difference between the two input voltages is called differential amplifier.
Key point: For very small Vd , output gets driven into saturation due to high AOL , hence this application is applicable for very small range of differential input voltage.

## Slide 86: Inverting Amplifier
The amplifier in which the output is inverted i.e. having 180o phase shift with respect to the input is called an inverting amplifier
Vo = -AOL Vin2
Keypoint: The negative sign indicates that there is phase shift of 180o between input and output i.e. output is inverted with respect to input.

## Slide 87: Non-inverting Amplifier
The amplifier in which the output is amplified without any phase shift in between input and output is called non inverting amplifier
Vo = AOL Vin1
Keypoint: The positive output shows that input and output are in phase and input is amplified AOL times to get the output.

## Slide 88: Why op-amp is generally not used in open loop mode?
As open loop gain of op-amp is very large, very small input voltage drives the op-amp voltage to the saturation level. Thus in open loop configuration, the output is at its positive saturation voltage (+Vsat ) or negative saturation voltage (-Vsat ) depending on which input V1 or V2 is more than the other. For a.c. input voltages, output may switch between positive and negative saturation voltages

## Slide 89
This indicates the inability of op-amp to work as a linear small signal amplifier in the open loop mode. Hence the op-amp in open loop configuration is not used for the linear applications

## Slide 90: General purpose op-amp 741
The IC 741 is high performance monolithic op-amp IC. It is available in 8pin, 10pin or 14pin configuration. It can operate over a temperature of -550 C to 1250 C.
Features:
No frequency compensation required
Short circuit protection provided
Offset Voltage null capability
Large common mode and differential voltage range
No latch up

## Slide 91
Internal schematic of 741 op-amp

## Slide 92
The 8pin DIP package of IC 741

## Slide 93: Realistic simplifying assumptions
Zero input current: The current drawn by either of the input terminals (inverting and non-inverting) is zero
Virtual ground :This means the differential input voltage Vd between the non-inverting and inverting terminals is essentially zero. (The voltage at the non inverting input terminal of an op-amp can be realistically assumed to be equal to the voltage at the inverting input terminal

## Slide 94: Closed loop operation of op-amp
The utility of the op-amp can be increased considerably by operating in closed loop mode. The closed loop operation is possible with the help of feedback. The feedback allows to feed some part of the output back to the input terminals. In the linear applications, the op-amp is always used with negative feedback. The negative feedback helps in controlling gain, which otherwise drives the op-amp out of its linear range, even for a small noise voltage at the input terminals

## Slide 95: Ideal Inverting Amplifier
The output is inverted with respect to input, which is indicated by minus sign.
The voltage gain is independent of open loop gain of the op-amp, which is assumed to be large.
The voltage gain depends on the ratio of the two resistances. Hence selecting Rf and R1 , the required value of gain can be easily obtained.
If Rf > R1,, the gain is greater than 1
If Rf < R1,, the gain is less than 1
If Rf = R1, the gain is unity
Thus the output voltage can be greater than, less than or equal to the input voltage in magnitude

## Slide 96
If the ratio of Rf and R1 is K which is other than one, the circuit is called scale changer while for Rf/R1 =1 it is called phase inverter.
The closed loop gain is denoted as AVF or ACL i.e. gain with feedback

## Slide 97: Ideal Non-inverting Amplifier
The voltage gain is always greater than one
The voltage gain is positive indicating that for a.c. input, the output and input are in phase while for d.c. input, the output polarity is same as that of input
The voltage gain is independent of open loop gain of op-amp, but depends only on the two resistance values
The desired voltage gain can be obtained by selecting proper values of Rf and R1

## Slide 98: Comparison of the ideal inverting and non-inverting op-amp
Ideal Inverting amplifier | Ideal non-inverting amplifier
1. Voltage gain=-Rf/R1 | 1. Voltage gain=1+Rf/R1
2. The output is inverted with respect to input | 2. No phase shift between input and output
3. The voltage gain can be adjusted as greater than, equal to or less than one | 3. The voltage gain is always greater than one
4. The input impedance is R1 | 4. The input impedance is very large

## Slide 99: Parameter consideration for various applications
For A.C. applications | For D.C. applications
Input resistance | Input resistance
Output resistance | Output resistance
Open loop voltage gain | Open loop voltage gain
Slew rate | Input offset voltage
Output voltage swing | Input offset current
Gain- bandwidth product | Input offset voltage and current drifts
Input noise voltage and current | 
Input offset voltage and current drifts | 

## Slide 100
Factors affecting parameters of Op-amp
Supply Voltage
Frequency
Temperature
Voltage gain
Output Voltage swing
Input voltage range
Power consumption
Input offset current
Voltage gain
Input resistance
Output resistance
CMRR
Input noise voltage
Input noise current
Input offset current
Input offset voltage
Input bias current
Power consumption
Gain-Bandwidth product
Slew rate
Input resistance

## Slide 101: Practical Inverting Amplifier
Closed Loop Voltage gain =

## Slide 102: Practical Non-Inverting Amplifier
Closed Loop Voltage gain =

## Slide 103
The End