## Slide 1: UNIT – I:Concepts in machine element dynamics

## Slide 2: CO 1
Student will be able to explain D’Alembert principle, precession and gyroscopic couple and determine the direction and effect of gyroscopic couple by analyzing various applications.

## Slide 3
The inertia force is an imaginary force, which when acts upon a rigid body, brings it in an equilibrium position. It is numerically equal to the accelerating force in magnitude, but opposite in direction.
Mathematically, Inertia force = – Accelerating force = – m.a
Where, m = Mass of the body, and a = Linear acceleration of the centre of gravity of the body.

## Slide 4
Similarly, the inertia torque is an imaginary torque, which when applied upon the rigid body, brings it in equilibrium position. It is equal to the accelerating couple in magnitude but opposite in direction.

## Slide 5
Dynamic Forces: Dynamic forces are associated with accelerating masses. As all machines have some accelerating parts, dynamic forces are always present when the machine operate. In case of rotors which rotates at speed more than 80,000 rpm, even slightest eccentricity of centre of mass from axis of rotation induces very high dynamic forces. This may lead to vibration, wear, noise or even failure.

## Slide 6: D-Alembert’s Principle
The vector sum of all external forces and inertia forces acting upon a system of rigid bodies is zero. The vector sum of all external moments and inertia torques acting upon a system of rigid bodies is also separately zero.
Inertia is a property of matter by virtue of which a body resists any change in velocity.
Inertia Force, Fi= -m.a (m: mass of body; a: acceleration of centre of mass of the body)
Negative sign indicates that the force acts in the opposite direction to that of acceleration. The force acts through centre of mass of the body.

## Slide 7: Gyroscopic Torque (Couple)

## Slide 8
Problem :
An aeroplane makes a complete half circle of 50 metres radius, towards left, when flying at 200 km per hr. The rotary engine and the propeller of the plane have a mass of 400 kg and a radius of gyration of 0.3 m. The engine rotates at 2400 r.p.m. clockwise when viewed from the rear. Find the gyroscopic couple on the aircraft and state its effect on it.