## Slide 1: ROCKET PROPELLANTS
PREPARED BY DR. SHAHBAZ KHAN
B.E. SECOND SEMESTER MATERIAL CHEMISTRY

## Slide 2: Rocket Propellants: -
Propellants are defined as substance or mixtures of substances of an explosive nature in a solid and liquid state that burn exothermally without contact with atmospheric oxygen and form a large volume of gas.
Characteristic of good Propellant:-
It should produce high temp on combustion.
It should burn at slow and steady rate.
It should be state to handle and store under ordinary conditions.
It should be non corrosive and non-hygroscopic.
It should leave no solid residue after ignition

## Slide 3: Principal of Rocket Propellant:-
The principal of Rocket Propellant depends on the following two laws.
Newton’s third law of motion : (Every action has an equal and opposite direction).
Law of conservation at momentum:
A rocket engine is generally throw Mass in the form of a high pressure gas. The engine throws the mass of gas out in one direction in one order to get a reaction in the opposite direction. This develop required thrust (Thrust is the force which moves any aircraft through the air).
This thrust development in a rocket is an interesting application of Newton’s third law of motion and momentum principals.
From the momentum point of view the hot gasses acquire momentum in forward direction. The burning process accelerates the mass of fuel so that it comes out of rocket nozzle at high speed. The fact that the fuel turns from a solid or liquid into a gas when it burns does not change its mass. Here law of conservation of momentum is applied.

## Slide 4: PROPULSION PRINCIPLE

## Slide 5: Classification of Propellants:-
Solid Propellants:-
Solid propellants rockets are basically combustion chamber tubes packed with a propellant that contains both fuel and oxidizer blended together uniformly.
The principal advantage is that a solid propellant is relatively stable therefore it can be manufacture and stored for future use.
Solid propellants have a high density and can burn very fast. They are relatively insensitive to shock, vibration and acceleration. No propellant pumps are required.
Disadvantages are that once ignited, burn until all the propellant is used. Cracks in the in the solid propellant increase the exposed surface area.
Manufacture of a solid propellant is an expensive.

## Slide 6: Liquid Propellants:-
Liquid propellants contain the fuel and oxidizer as a single substance or mixture of substance (Mono) or in two separate phases (bipropellants). They are more advantageous for use than the solid propellants and so their uses are more versatile.
Types of Liquid Propellants:-
Mono Propellants
Bi-Propellants
Hybrid Propellants

## Slide 7: Mono Propellants:-
Mono Propellants combine the properties of fuel and oxidizer in one chemical. By their nature monopropellants are unstable and dangerous.

## Slide 8: Bi-Propellants:-
Bipropellants consist of an oxidizer and a fuel that are injected in two separate phases to the combustion chamber. Commonly used oxidizers are O3, liquid O2, etc.

## Slide 9: Hybrid Propellants:-
In hybrid propellants the compound are present in different states of aggregation, for example, a liquid oxidizer and solid fuel or a solid oxidizer and a liquid fuel these propellants occupy an intermediate position between liquid and solid propellants. They have higher specific impulse. Their combustion is controllable but they are hard to store and maintain.

## Slide 10: THANK YOU